## Slide 1
01
ARCGIS PRO · RASTER ANALYSIS
Raster Data
Analysis
Turn a grid of cell values into terrain, vegetation and decision surfaces — three core techniques, taught with free U.S. data and ArcGIS Pro tools.
SURFACE ANALYSIS
Slope, aspect & hillshade from an elevation grid (DEM).
MAP ALGEBRA
Cell-by-cell math to combine and transform raster values.
SUITABILITY MODELING
Weighted overlay to rank the best places for a goal.
Click a card above to jump straight to that section →

## Slide 2
RASTER DATA ANALYSIS
02
What is raster data?
A continuous grid of equal-sized cells — every cell holds a value
HOW A RASTER STORES THE WORLD
A grid of cells
The area is divided into equal-sized square cells (pixels), each holding one value.
Cell size = resolution
Smaller cells capture finer detail — but create larger files.
Bands
Cells can stack several values at once, e.g. RGB or multispectral imagery.
A continuous field
Values exist everywhere on the grid — ideal for surfaces and imagery.
COMMON FILE FORMATS
GeoTIFF (.tif, .tiff) — the universal georeferenced raster
Esri GRID — native ArcGIS raster, stored as a folder
ERDAS IMAGINE (.img) — common for satellite imagery
ASCII Grid (.asc) — plain-text, portable and readable
JPEG 2000 (.jp2) — heavily compressed imagery
netCDF / HDF (.nc, .hdf) — multidimensional scientific data

## Slide 3
RASTER DATA ANALYSIS
03
Learning objectives
What you'll be able to do by the end of this lesson
Read a DEM & derive surfaces
Turn an elevation grid into slope, aspect, hillshade and contour lines.
Do cell-by-cell map algebra
Combine and transform rasters with local, focal, zonal and global operations.
Build a suitability model
Reclassify, weight and overlay criteria to rank the best locations for a goal.
Find free U.S. data
Source DEMs, imagery and land cover from USGS 3DEP, NLCD and NREL.
Choose the right tool
Match each task to the correct ArcGIS Pro Spatial Analyst tool.

## Slide 4
RASTER DATA ANALYSIS
04
Three ways to analyze a raster
Pick the family of operations that answers your question
SURFACE ANALYSIS
Derive slope, aspect, hillshade and contours from an elevation grid.
CORE TOOL
Spatial Analyst · Surface
e.g. Central Park, NYC
MAP ALGEBRA
Run cell-by-cell math to combine and transform raster values.
CORE TOOL
Spatial Analyst · Map Algebra
e.g. NDVI, Central Valley
SUITABILITY MODELING
Reclassify, weight and overlay criteria to rank the best sites.
CORE TOOL
Spatial Analyst · Overlay
e.g. Solar siting, Arizona

## Slide 5
05
SECTION 01
Surface Analysis
Turn a single elevation grid into the shape of the land — slope, aspect, shaded relief and contour lines.
SLOPE
ASPECT
HILLSHADE
CONTOURS

## Slide 6
SURFACE ANALYSIS
06
From elevation to terrain
Every surface tool derives a brand-new raster from a DEM's cell values
DERIVED SURFACES
Slope
Steepness of each cell, in degrees or percent rise.
Aspect
The compass direction a slope faces, 0–360°.
Hillshade
Shaded relief from a light source — realistic terrain.
Contours
Lines joining cells of equal elevation.
HOW IT WORKS
Each tool scans a moving 3×3 window of cells and computes a value from that neighbourhood — so every result is itself a new raster.
WHERE TO FIND IT IN ARCGIS PRO
Analysis ▸ Tools ▸ Spatial Analyst ▸ Surface
Slope · Aspect · Hillshade · Contour
Tip: or type a tool name into the Geoprocessing search.

## Slide 7
SURFACE ANALYSIS
07
Central Park, NYC — a 1 m DEM
From an elevation grid to slope, aspect and shaded relief
Central Park, New York City
1 m DEM · USGS 3DEP
DEM → hillshade → slope · aspect
WORKFLOW
Get the DEM
Download the 1 m elevation model for Central Park from USGS 3DEP (The National Map).
Derive surfaces
Run Slope, Aspect and Hillshade on the DEM with Spatial Analyst → Surface.
Read the terrain
Vista Rock rises ~40 m above the low-lying Pool, Loch and Ravine to the north.
FREE DATA SOURCE
USGS 3DEP 1 m DEM — The National Map (apps.nationalmap.gov)

## Slide 8
SURFACE ANALYSIS · HANDS-ON LAB
08
Your turn — map the terrain
Derive slope, aspect and hillshade from the Central Park DEM
TASK
1
Add the Central Park 1 m DEM to a new map in ArcGIS Pro.
2
Run Slope (Spatial Analyst ▸ Surface) with output in degrees.
3
Run Aspect on the DEM to map the direction each slope faces.
4
Run Hillshade with azimuth 315° and altitude 45°.
5
Use Explore to click Vista Rock and read its elevation.
ANSWER KEY
Step 2 — Slope highlights the steep banks of the Ravine and Great Hill.
Step 4 — Hillshade renders a 3-D shaded relief of the park.
Step 5 — Vista Rock reads about 40 m — the park's high point.
Click to reveal the Answer Key
(plays in Slide Show)
EXPECTED RESULT
You can turn one elevation grid into slope, aspect and hillshade rasters — and read real elevations — fully describing Central Park's terrain from a DEM.
Click to reveal the Expected Result
(plays in Slide Show)

## Slide 9
09
SECTION 02
Map Algebra
Do math on raster cells — combine, transform and reclassify grids to build brand-new value surfaces.
LOCAL
FOCAL
ZONAL
GLOBAL

## Slide 10
MAP ALGEBRA
10
Four kinds of raster math
How map algebra transforms grids of cell values
OPERATION TYPES
Local
Cell-by-cell math on one or more grids at the same location — add, reclassify, NDVI.
Focal
Reads a moving neighbourhood window — smoothing, focal mean, edge detection.
Zonal
Summarises cells inside zones — e.g. mean elevation per watershed.
Global
Uses the whole raster — Euclidean distance, cost path, region groups.
HOW IT WORKS
Map algebra evaluates an expression on every cell. The output is always a new raster the same size and grid as the input(s).
WHERE TO FIND IT IN ARCGIS PRO
Spatial Analyst ▸ Map Algebra ▸ Raster Calculator
Toolsets: Local · Focal · Zonal · Global
Tip: build formulas like (NIR - Red) / (NIR + Red).

## Slide 11
MAP ALGEBRA
11
NDVI in California’s Central Valley
Cell-by-cell band math turns two Landsat bands into a vegetation index
California’s Central Valley
NDVI · Landsat 8 / 9
( NIR − Red ) / ( NIR + Red )
WORKFLOW
Get the bands
Download a Landsat 8/9 scene — the Red and Near-Infrared bands — from USGS EarthExplorer.
Run the band math
In Raster Calculator, compute (NIR − Red) / (NIR + Red) as a Float raster.
Read the index
Values near +1 are lush irrigated cropland; near 0 is bare desert soil.
FREE DATA SOURCE
USGS EarthExplorer — Landsat 8/9 Collection 2 (earthexplorer.usgs.gov)

## Slide 12
MAP ALGEBRA · HANDS-ON LAB
12
Your turn — compute NDVI
Turn two Landsat bands into a vegetation index with Raster Calculator
TASK
1
Add the Landsat Red and NIR bands to a new map in ArcGIS Pro.
2
Open Raster Calculator (Spatial Analyst ▸ Map Algebra).
3
Enter Float(NIR − Red) / Float(NIR + Red) and run it.
4
Apply a green colour ramp and stretch it to the value range.
5
Use Explore to click a cropland cell, then a desert cell, and compare.
ANSWER KEY
Step 3 — wrap bands in Float() so you get decimals, not integers.
Step 4 — NDVI ranges about −1 to +1; stretch the ramp to fit.
Step 5 — cropland ≈ 0.6–0.9; bare desert ≈ 0–0.2.
Click to reveal the Answer Key
(in Slide Show)
EXPECTED RESULT
You can compute NDVI with map algebra and read vegetation vigour cell-by-cell — high over irrigated fields, low over desert.
Click to reveal the Expected Result
(in Slide Show)

## Slide 13
13
SECTION 03
Suitability Modeling
Blend several factors into one score — reclassify each layer to a common scale, weight them, and overlay to rank the best places.
CRITERIA
RECLASSIFY
WEIGHT
OVERLAY

## Slide 14
SUITABILITY MODELING
14
The weighted-overlay workflow
Blend several criteria rasters into one suitability score
FOUR STEPS
Define criteria
List the factors that make a site good or bad — slope, land cover, distance.
Reclassify
Rescale every input raster onto one common suitability scale, e.g. 1–9.
Weight
Give each criterion an importance weight; the weights sum to 100%.
Overlay & score
Combine the weighted layers into a single suitability surface.
HOW IT WORKS
Each reclassified layer is multiplied by its weight and added — so every cell ends up with one suitability score.
WHERE TO FIND IT IN ARCGIS PRO
Spatial Analyst ▸ Overlay ▸ Weighted Overlay
Also: Reclass ▸ Reclassify · Distance tools
Tip: Weighted Sum works too when weights are raw multipliers.

## Slide 15
SUITABILITY MODELING
15
Siting a solar farm in Arizona
Four criteria layers, weighted and overlaid into one suitability map
Arizona, USA
Utility-scale solar siting
high sun · flat ground · open land · near grid
WORKFLOW
Gather the criteria
Slope (3DEP), land cover (NLCD), solar resource (NREL GHI) and distance to transmission lines.
Reclassify & weight
Rescale each layer to 1–9; weight solar resource and slope the highest.
Overlay & rank
Weighted Overlay yields a 1–9 map — the 8–9 zones are the best sites.
FREE DATA SOURCES
USGS 3DEP · MRLC NLCD · NREL NSRDB — all free (nrel.gov, mrlc.gov)

## Slide 16
SUITABILITY MODELING · HANDS-ON LAB
16
Your turn — model solar suitability
Weight and overlay four criteria to rank the best solar sites in Arizona
TASK
1
Add slope (3DEP), NLCD land cover, NREL solar (GHI) and transmission lines.
2
Reclassify each raster to a 1–9 suitability scale (Spatial Analyst ▸ Reclass).
3
Open Weighted Overlay (Spatial Analyst ▸ Overlay).
4
Set weights — e.g. GHI 40%, slope 30%, land cover 20%, access 10%.
5
Run it, symbolise the 1–9 output and highlight the 8–9 cells.
ANSWER KEY
Step 2 — flat land with high GHI scores 9; steep or protected land scores 1.
Step 4 — the weights must add up to 100%.
Step 5 — the 8–9 cells are your most suitable solar sites.
Click to reveal the Answer Key
(in Slide Show)
EXPECTED RESULT
You can turn four criteria rasters into one weighted suitability map and point to the best solar-farm sites in Arizona.
Click to reveal the Expected Result
(in Slide Show)

## Slide 17
RASTER DATA ANALYSIS
17
Choosing a raster tool
Match the technique to the question you're asking
RASTER TASK
SURFACE ANALYSIS
MAP ALGEBRA
SUITABILITY
The question
What shape is the land?
What do cells add up to?
Where is the best place?
Core operation
Neighbourhood 3×3 on a DEM
Cell-by-cell raster math
Reclassify + weighted overlay
Key input
One elevation grid (DEM)
One or more value rasters
Several criteria rasters
Output
Slope · aspect · hillshade
New value raster (NDVI)
A 1–9 suitability map
ArcGIS tool
Spatial Analyst ▸ Surface
Raster Calculator
Weighted Overlay
Example & data
Central Park · 3DEP
Central Valley · Landsat
Arizona · NLCD · NREL

## Slide 18
RASTER DATA ANALYSIS
18
Knowledge check
Click each card in Slide Show to reveal the answer
1
Which tool gives a shaded-relief image of terrain?
Hillshade — it lights the DEM from a set sun angle to show relief.
Click to reveal answer
2
In NDVI, what does a value near +1 mean?
Dense, healthy vegetation; values near 0 mean bare ground.
Click to reveal answer
3
Why reclassify every layer before a weighted overlay?
To put all criteria on one common suitability scale, e.g. 1–9.
Click to reveal answer
4
Is NDVI a local, focal, zonal or global operation?
Local — it works cell-by-cell at the same location in each band.
Click to reveal answer

## Slide 19
RASTER DATA ANALYSIS
19
Recap — and what's next
You can now read, transform and combine rasters to answer real questions
Three techniques
Surface analysis, map algebra and suitability all turn cells into insight.
Output is a raster
Every tool reads cell values and writes a brand-new grid.
Free U.S. data
3DEP, Landsat, NLCD and NREL cover the whole country.
One toolbox
It all lives in ArcGIS Pro's Spatial Analyst extension.
UP NEXT
Interpolation & Surfaces
Turn scattered field measurements into continuous rasters — then feed them into the analyses you just learned.
Sample points → continuous grid
IDW and Kriging methods
Spatial Analyst ▸ Interpolation