## Slide 1
ARCGIS PRO · GEOPROCESSING TOOLS
Geoprocessing Tools
Four core vector operations — Buffer, Clip, Dissolve, and Overlay — that turn raw layers into spatial answers.
B
Buffer
Zones of proximity
C
Clip
Cookie-cutter extract
D
Dissolve
Merge by attribute
O
Overlay
Union · Intersect
01 / 23
Click a tool below to jump straight to that section →

## Slide 2
ARCGIS PRO · GEOPROCESSING TOOLS
02 / 23
What we'll cover
A guided tour — from fundamentals to a full working pipeline
01
Foundations
What geoprocessing is, the ArcGIS Pro environment, and geometry types.
02
Buffer
Build distance zones of proximity around features.
03
Clip
Trim a layer to the outline of a study area.
04
Dissolve
Merge features that share an attribute value.
05
Overlay
Combine two layers with Union and Intersect.
06
In practice
A comparison, a hands-on lab, and a knowledge check.
Click any topic below to jump straight to that section →

## Slide 3
ARCGIS PRO · GEOPROCESSING TOOLS
03 / 23
Learning objectives
What you'll be able to do by the end of this lesson
1
Frame the toolkit
See how Buffer, Clip, Dissolve and Overlay fit together as a workflow.
2
Build proximity zones
Use Buffer to create distance-based areas around points, lines or polygons.
3
Extract by boundary
Use Clip to cut a working layer down to a study-area outline.
4
Simplify by attribute
Use Dissolve to merge adjacent features that share the same value.
5
Combine two layers
Use Union and Intersect to overlay layers and blend their attributes.

## Slide 4
ARCGIS PRO · GEOPROCESSING TOOLS
04 / 23
What is geoprocessing?
Operations that take spatial layers in and write brand-new layers out
INPUT
Feature layers
One or more existing layers — points, lines or polygons on your map.
OPERATION
A geoprocessing tool
A defined spatial rule with parameters you set before it runs.
OUTPUT
A new layer
A fresh dataset written to disk; the inputs stay untouched.
Non-destructive by design — every tool writes a new output layer and leaves your source data completely untouched.

## Slide 5
ARCGIS PRO · GEOPROCESSING TOOLS
05 / 23
The geoprocessing environment
Where these tools live — and how you run them — in ArcGIS Pro
THE GEOPROCESSING PANE
Open a tool, fill in its parameters, and click Run. Every tool reads existing layers and writes a brand-new output — added straight to your map.
1
Search the tool by name
in the Geoprocessing pane
2
Set inputs & parameters
distance, fields, tolerances…
3
Check Environments
output coordinate system, extent, mask
4
Run — output is added
and logged in the History
THREE WAYS TO RUN A TOOL
Geoprocessing pane
One tool at a time, interactively — the everyday way to work.
ModelBuilder
Chain many tools into a visual, reusable workflow you can re-run.
Batch & Python
Run one tool across many datasets, or automate with arcpy scripting.

## Slide 6
ARCGIS PRO · GEOPROCESSING TOOLS
06 / 23
Geometry types & compatibility
What each tool accepts as input — and the geometry it returns
TOOL
POINT
LINE
POLYGON
OUTPUT
Buffer
Polygon buffer zones
Clip
Same geometry, trimmed to the boundary
Dissolve
Fewer, merged features
Overlay
Polygon (line where it crosses a polygon)
supported input
not a typical input

## Slide 7
ARCGIS PRO · GEOPROCESSING TOOLS
07 / 23
The four tools at a glance
One color per tool — carried through the rest of the deck
B
Buffer
Creates a zone a set distance around features.
e.g. 500 m around every well
C
Clip
Cuts a layer to the outline of another layer.
e.g. roads inside one county
D
Dissolve
Merges features that share an attribute value.
e.g. counties → states
O
Overlay
Combines two layers — Union keeps all, Intersect keeps the shared part.
e.g. soils × zoning

## Slide 8
ARCGIS PRO · GEOPROCESSING TOOLS
08 / 23
Buffer
Zones of proximity around your features
HOW IT WORKS
Buffer draws a new polygon at a fixed distance around each input feature — the classic way to ask “what lies within X?”
1
Choose input features — points, lines or polygons.
2
Set a distance and units, e.g. 500 metres.
3
Optionally dissolve overlapping rings into one zone.
WHEN TO USE
Noise contours, catchment areas, protective setbacks and service radii.
SCHEMATIC
d
Point → circular zone
Line → capsule zone
A zone of the chosen radius wraps every feature; overlapping zones can be dissolved into one.

## Slide 9
ARCGIS PRO · GEOPROCESSING TOOLS
09 / 23
Buffer — key parameters
The settings that decide the size, shape and count of your zones
Distance
VALUE · FIELD
A single distance, or read a different distance per feature from a field.
Method
PLANAR · GEODESIC
Planar for local projected data; geodesic for large areas or lat–long.
Side Type
FULL · LEFT · RIGHT · OUTSIDE
Which side of a line or polygon to build the zone on.
End Type
ROUND · FLAT
How the ends of buffered lines are capped.
Dissolve Type
NONE · ALL · LIST
Merge overlapping buffers into one seamless zone — or keep them separate.
Multi-Ring
100 · 250 · 500 m
A separate tool for several distances at once — nested proximity bands.

## Slide 10
ARCGIS PRO · GEOPROCESSING TOOLS
10 / 23
Buffer in action
Mapping a stream-protection corridor
THE TASK
A county bans building within 50 m of any stream. Planners need that no-build corridor mapped as a single, seamless layer.
TOOL RECIPE
Input
Streams (line)
Distance
50 Meters
Method
Geodesic
Dissolve Type
ALL
Result one continuous riparian buffer, ready to overlay with parcels to flag conflicts.
SCHEMATIC
BEFORE
AFTER
The 50 m zone, dissolved with ALL, becomes one seamless polygon.

## Slide 11
ARCGIS PRO · GEOPROCESSING TOOLS
11 / 23
Clip
Cut a layer to the shape of a boundary
HOW IT WORKS
Clip keeps only the parts of an input layer that fall inside a second boundary — a cookie-cutter for spatial data.
1
Pick the input layer you want to trim.
2
Pick a clip boundary — the cutter shape.
3
Output keeps only what lies inside it.
WHEN TO USE
Trim national data down to your study area — a county, watershed or project extent.
SCHEMATIC
kept
Everything inside the boundary is kept; features outside are dropped from the output.

## Slide 12
ARCGIS PRO · GEOPROCESSING TOOLS
12 / 23
Clip — parameters & cousins
A cookie-cutter for spatial data — and the tools it's mistaken for
PARAMETERS
Input Features
The layer to be trimmed — points, lines or polygons.
Clip Features
The cutting boundary. Must be a polygon layer.
XY Tolerance
Optional. Snap distance for coincident boundaries.
Clip copies geometry only — it never adds the boundary layer's attributes.
EASY TO CONFUSE WITH
Erase
Keeps what lies OUTSIDE the polygon — Clip's mirror image.
Split
Cuts the input into many layers, one per attribute value.
Intersect
An overlay that also JOINS attributes from both inputs.
Clip = keep INSIDE, no attribute join. That's the whole difference.

## Slide 13
ARCGIS PRO · GEOPROCESSING TOOLS
13 / 23
Clip in action
Extracting just the roads inside one county
THE TASK
A statewide roads layer is far too big. A local study only needs the roads that fall inside Travis County.
TOOL RECIPE
Input Features
Roads (line)
Clip Features
County boundary (polygon)
Output
Roads_TravisCo
Result roads that stop exactly at the county line — smaller and faster.
SCHEMATIC
BEFORE
AFTER
Only the segments inside the boundary survive; everything outside is dropped.

## Slide 14
ARCGIS PRO · GEOPROCESSING TOOLS
14 / 23
Dissolve
Merge features that share a value
HOW IT WORKS
Dissolve erases the boundaries between adjacent features that share an attribute value, combining many into few.
1
Choose the input polygon layer.
2
Pick a field to group by (the dissolve field).
3
Shared boundaries between matching features vanish.
WHEN TO USE
Roll counties up into states, parcels into zones, or tidy split polygons.
SCHEMATIC
BEFORE
6 features
AFTER
2 features
Adjacent features with the same value merge into one; the grouping attribute is kept.

## Slide 15
ARCGIS PRO · GEOPROCESSING TOOLS
15 / 23
Dissolve — parameters
The settings that control how — and how much — your features merge
Dissolve Field(s)
ONE OR MORE FIELDS
Group by attributes; features sharing the value merge into one.
Statistics Fields
SUM · MEAN · MIN · MAX · COUNT
Summarise an attribute for each merged group.
Create Multipart
ON · OFF
ON keeps scattered same-value areas as one multipart feature.
Unsplit Lines
Merge connected line segments that share values — geometry preserved.
No Dissolve Field
= ONE FEATURE
Leave it blank and the whole layer melts into a single feature.
What You Get
Fewer features, clean boundaries, and roll-up stats in the table.

## Slide 16
ARCGIS PRO · GEOPROCESSING TOOLS
16 / 23
Dissolve in action
Rolling counties up into states
THE TASK
A layer of hundreds of county polygons must become one polygon per state — with each state's population totalled.
TOOL RECIPE
Input
Counties (polygon)
Dissolve Field
STATE
Statistics
SUM of POP
Multipart
ON
Result one polygon per state, each carrying its total population.
SCHEMATIC — DISSOLVE BY STATE
BEFORE
AFTER
Counties sharing a STATE value merge; their populations are summed.

## Slide 17
ARCGIS PRO · GEOPROCESSING TOOLS
17 / 23
Overlay — Union & Intersect
Two ways to combine a pair of layers into a single new layer
Union
A ∪ B
Layer A
Layer B
Output covers both layers combined
Attributes from A and B are joined
Intersect
A ∩ B
Layer A
Layer B
Output keeps only the shared overlap
A feature must exist in both layers

## Slide 18
ARCGIS PRO · GEOPROCESSING TOOLS
18 / 23
Overlay — parameters & behaviour
How Union and Intersect combine two layers — geometry and attributes
PARAMETERS
Input Features
Two or more polygon layers to combine.
Join Attributes
ALL · NO_FID · ONLY_FID — which fields reach the output.
XY Tolerance
Snap distance for coincident boundaries.
Output Type
INPUT · LINE · POINT — dimension of the result.
SAME FAMILY: IDENTITY · SYMMETRICAL DIFFERENCE · ERASE · UPDATE
UNION vs INTERSECT
Union
A ∪ B
Keeps ALL area from both inputs. Outside the overlap, the other layer's fields are left null.
Intersect
A ∩ B
Keeps ONLY the overlapping area. Every output feature carries attributes from both layers.
Both stamp a combined attribute row on every output — the real payoff over a plain Clip.

## Slide 19
ARCGIS PRO · GEOPROCESSING TOOLS
19 / 23
Overlay in action
Where do prime soils and agricultural zoning agree?
THE TASK
Find every area that is BOTH prime farmland (soils) AND zoned agricultural — the land most worth protecting.
TOOL RECIPE
Inputs
Soils + Zoning (polygon)
Tool
Intersect
Join Attributes
ALL
Result polygons that are prime AND agricultural, tagged with both soil class and zoning code.
SCHEMATIC — INTERSECT
BEFORE
AFTER
Soils
Zoning
kept: both
Intersect keeps only where both layers coincide — tagged with both tables.

## Slide 20
ARCGIS PRO · GEOPROCESSING TOOLS
20 / 23
Choosing the right tool
Four operations, four different spatial jobs
Tool | Input | Key setting | Output | Typical question
Buffer | Point / line / polygon | Distance + units | Polygon zones | What lies within X of this?
Clip | Layer + boundary | Clip feature | Trimmed input | What falls inside my area?
Dissolve | Polygons | Field to group by | Fewer merged polygons | Can I merge by category?
Overlay | Two layers | Union or Intersect | Combined layer | How do two layers relate?

## Slide 21
ARCGIS PRO · GEOPROCESSING TOOLS
21 / 23
Your turn — hands-on lab
Chain all four tools into one workflow in ArcGIS Pro
TASK
Flag schools within 500 m of a flood zone and inside the city limits — counted by district.
1
Add the schools, flood-zone and city-boundary layers to your map.
2
Buffer the flood zone by 500 m (Method: Geodesic, Dissolve: ALL).
3
Clip the schools layer to the city boundary.
4
Intersect the clipped schools with the flood buffer.
5
Dissolve the result by district to count schools per area.
ANSWER KEY
Step 2 — Geodesic + Dissolve ALL make one clean corridor.
Step 4 — Intersect keeps only schools inside the buffer.
Step 5 — Dissolve by district adds a COUNT per area.
EXPECTED RESULT
A short, per-district list of flood-exposed schools — produced by chaining Buffer → Clip → Intersect → Dissolve into one repeatable model you can re-run any time.
▸ Click to reveal the Answer Key
▸ Click to reveal the Expected Result

## Slide 22
ARCGIS PRO · GEOPROCESSING TOOLS
22 / 23
Knowledge check
Match each task to the right tool — then click to reveal the answer
1
QUESTION 1
Flag every parcel within 300 m of a river.
2
QUESTION 2
Keep only the roads that lie inside a national park.
3
QUESTION 3
Turn 254 county polygons into one polygon per state, with totals.
4
QUESTION 4
Keep only where soils AND zoning overlap, tagged with both.
Buffer — build a 300 m zone around the rivers, then select the parcels that fall inside.
Clip — trim the roads to the park boundary; the attributes stay unchanged.
Dissolve — group by the STATE field; add a SUM statistic for the totals.
Overlay → Intersect — the output carries attributes from both input layers.
▸ Click to reveal answer
▸ Click to reveal answer
▸ Click to reveal answer
▸ Click to reveal answer

## Slide 23
ARCGIS PRO · GEOPROCESSING TOOLS
23 / 23
Recap & what's next
The four tools at a glance — and where the trail leads
IN A NUTSHELL
Buffer
distance zones drawn around features
Clip
trims a layer to the shape of a boundary
Dissolve
merges features that share an attribute
Overlay
unions or intersects two layers into one
Non-destructive by design — every tool writes a new layer and leaves your source data intact.
UP NEXT
Raster Analysis
Surface analysis Slope, aspect & hillshade from a DEM
Map algebra Cell-by-cell math on raster values
Suitability modeling Weighted overlay to rank the best places
Continue the series